## Slide 1: Storage Workload Profile
SJEMCDEV01 As of 2015-02-01

## Slide 2: Warning Summary
Message
This data did not contain a Clariion/VNX SPCollect, or contained an SPCollect from before FLARE 28. The SPCollect provides detailed configuration information, including unbound and spare drives.

## Slide 3: Scan Summary
Name | Model | Software Level | Serial Number | Start Date | End Date | Interval (min)
APM00140712253 | VNX5800 | 7.33.3.0.74 | APM00140712253 | 2015-01-31 14:04 | 2015-02-01 02:54 | 5

## Slide 4: WORKLOAD Profile Review WORKLOAD Profile Review
RESPONSE TIMES
READ / WRITE
PERFORMANCE
I/O SIZE
THROUGHPUT
CAPACITY
DATA SKEW

## Slide 5: Assets
Name | Model | Disk (TB) | EFD (TB) | Usable (TB) | Used (TB) | Utilization (%)
APM00140712253 | VNX5800 | 166.09 | 1.61 | 126 | 51 | 40
Drive Type | # Disks | % of IOPS | Raw Capacity (TB) | Raw Capacity (%)
FLASH | 9 | 72 | 2 | 1
SAS | 4 | 4 | 1 | 1
SAS | 45 | 23 | 36 | 22
NL | 48 | 0 | 129 | 77
 | 106 | 100 | 168 | 100
Notes: This slide lists all the assets found in the submitted data. It also includes the amount of IOPS by Drive Type, where applicable / when available.

## Slide 6: Workload Profile
Chart: Front End IOPS
 | 1
Date Time | Front End IOPS | Front End MBps | Read % | Avg Read Size (KB) | Avg Write Size (KB)
2015-01-31 14:09:51 | 8,123 | 281 | 51 | 32 | 39
2015-01-31 20:24:51 | 7,962 | 232 | 46 | 28 | 31
2015-01-31 22:59:52 | 10,384 | 353 | 49 | 31 | 39
2015-01-31 23:19:51 (95th) | 8,037 | 217 | 49 | 25 | 30
Three peak values have been selected to illustrate the busiest time periods.
Notes: The graph in this Workload Profile Slide illustrates the Front End IOPS as presented over a period of time. The table illustrates the Peak metrics at several points in time. This is meant to illustrate that different Metrics can peak at different times depending on the workload.

## Slide 7: Workload Profile Metrics
Name | APM00140712253
# Disks | 97
Disk (TB) | 166
EFD (TB) | 2
LUNs (TB) | 50
Used Capacity (TB) | 50
Skew | 86% of IOPS/15% of LUNs
Front End MBps - max | 402
Date Time - Peak | 2015-01-31
IOPS at Peak | 10,384
Read % At Peak | 49
Read Size (KB) at Peak | 31
Write Size (KB) at Peak | 39
MB/sec at Peak | 353

## Slide 8: 5 Year Growth Projections
Chart: Year
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Current Usable Capacity | 126.2773 | 126.2773 | 126.2773 | 126.2773 | 126.2773 | 126.2773
20% Growth (IDC Standard) | 50.8037 | 60.9645 | 73.1573 | 87.7888 | 105.3466 | 126.4159
30% Growth | 50.8037 | 66.0448 | 85.8583 | 111.6158 | 145.1005 | 188.6306
40% Growth | 50.8037 | 71.1252 | 99.5753 | 139.4054 | 195.1675 | 273.2346
At 30% growth, usable capacity will be exceeded in less than 4 year(s).
Notes: This slide displays the system’s current consumed capacity level in TB and graphs growth using different growth percentage rates including IDC standard of 20%. In addition, this slide estimates the expected time frame for an upgrade by using the IDC growth rate and system’s total usable capacity.

## Slide 9: Response Time
Chart: Front End IOPS
 | 1
Chart: Response Time (ms)
Average response time was 2ms, with a peak of 5ms

## Slide 10: LUN Skew - Front-End IOs
Chart: IOPS Rank
Pool 0 - Recoverpoint JVol | 12.52 | 11.52 | 10.68 | 10.33 | 8.95 | 8.9 | 8.82 | 7.41 | 6.3 | 6.08 | 5.65 | 5.3 | 3.85 | 1.71 | 1.7 | 1.7 | 1.7 | 1.69 | 1.68 | 0.07 | 0.07
86% of IOPS are to 15% of LUNs
Notes: This chart shows LUN Skew and NOT Sub-LUN Skew. This graph shows a high level view of skew and should be used to open a discussion around FAST and its benefits.

## Slide 11: Heat Map
Notes: Rockies
Color key:
  Blue: 0-19% utilization
  Cyan: 20-39% Utilization
  Green: 40-59% utilization
  Yellow: 60-79% utilization
  Orange: 80-89% utilization
  Red: 90-100% utilization
Top row shows port utilization, as a percentage of max bandwidth / port bandwidth. Port bandwidth is based on the currently negotiated bandwidth: ports may be capable of higher throughput. Max Bandwidth is the maximum of read or write bandwidth: this shows the maximum utilization in either direction.
The second row shows the SP Processor Utilization.
The third row depends on the FLARE Operating Environment version running on the system
  For pre-OE 33 (pre-VNX2) environments, this section shows the SP Dirty Pages Utilization %. Each SP maintains a separate cache, therefore two caches are shown
  For OE 33 (Rockies) and above, the SP Caches are unified, therefore the total SP Dirty Pages in MB is shown (the maximum of the values from each SP). The SP Dirty Pages are color coded according to the amount of Write Throttling: fewer than 10 write throttles per sec = blue, up to 50 then cyan, up to 100 then green, up to 200 then yellow, over 200 then orange.
These write throttle thresholds are chosen arbitrarily, to show the amount of cache activity within the system. It's expected and normal that a busy system will show more requests than an idle system
The fourth row shows bus utilization. This is calculated using the total disk bandwidth (MB/sec) for all disks on a given bus, and assumes a 4Gb/sec bus speed for CX systems and 6x4 Gb/sec bus speed for VNX systems. If the model is undetected, the model is assumed to be a CX.
The final set of rows shows disk utilization for each individual disk. Each disk is identified by three indicators: Raid Group, Speed, and Size. FC for the Raid Group value indicates a FAST Cache device. Each row represents a bus and target, identified by the leftmost label: b0e1 is Bus 0, Enclosure 1

## Slide 12: Flash Suitability Analysis

## Slide 13: Flash Suitability Analysis
This section classifies client / storage group workloads based on their workload profile at the client peak IOPS.
These scores are intended to help prioritize workloads to migrate to flash.
Clients are first grouped into three categories:
  High IOPS: 1000+ IOPS (at client peak)
  Medium-High IOPS: 500+ IOPS
  Moderate IOPS: 100+ IOPS
  Moderate-Low IOPS: 1+ IOPS
  Very Low IOPS: less than 1 IOPS
Clients are then scored based on their combined score on the following metrics:
  Response Time: 25ms+ (4 pts), 10-25ms (3 pts), 5-10ms (2 pts), 2-5ms (1 pt), 0-2ms (0 pts)
  Randomness: 75%+ (3 pts), 25-75% (2 pts), 0-25% (1 pt)
  Cache Misses: 75%+ (3 pts), 25-75% (2 pts), 0-25% (1 pt)
  IO Size: 0-16KB (3 pts), 16-64KB (2 pts), 64KB+ (1 pt)
See the notes section for more details

## Slide 14: Storage Profile
Chart: IOPS
Chart: Response Time (ms)
 | 1
At its busiest, this system is driving 10,384 IOPS at an average response time of 3ms
Flash storage can provide high IO rates with the lowest response time.
Flash storage can deliver consistent performance without resource contention.

## Slide 15: Classification (4) 1000+ IOPS
Client | Score | Response Time | Randomness | Cache Misses | IO Size | Front End IOPS | Used (TB)
sjsqlqa10 | 6 | Fast | N/A | High | Small | 1,173 | 0.39
sjemcrpa01, sjemcrpa02 | 5 | Medium | N/A | High | Large | 10,344 | 24.61
sapqas01 | 5 | Fast | N/A | High | Medium | 1,189 | 4.52
Analysis based on the point in time where the client reached it's highest/maximum IOPS.
Notes: Used Capacity: For Thin Devices, this is the consumed amount of space for each thin devices. For non-thin devices, this is the same as the LUN Capacity and shows the total allocated space.
Front End IOPS:
  High: 1000+ IOPS
  Medium: 500-1000 IOPS
  Low: 1-500 IOPS
  Idle: 0-1 IOPS
Response Time:
  Extremely Slow: 25+ ms
  Very Slow: 10+ ms
  Slow: 5+ ms
  Medium: 2+ ms
  Fast: 0-2ms
Randomness:
  Random: 75-100 Percent Random
  Mixed: 25-75 Percent Random
  Sequential: 0-25 Percent Random
Cache Misses:
  High: 75-100 Percent Misses
  Medium: 25-75 Percent Misses
  Low: 0-25 Percent Misses
IO Size:
  Small: 0-16KB
  Medium: 16-64KB
  Large: 64KB+

## Slide 16: Classification Medium (2) 100+ IOPS
Client | Score | Response Time | Randomness | Cache Misses | IO Size | Front End IOPS | Used (TB)
armstg01 | 6 | Medium | N/A | High | Medium | 399 | 3.60
bsmdbqa01 | 5 | Medium | N/A | High | Large | 327 | 2.28
Notes: Used Capacity: For Thin Devices, this is the consumed amount of space for each thin devices. For non-thin devices, this is the same as the LUN Capacity and shows the total allocated space.
Front End IOPS:
  High: 1000+ IOPS
  Medium: 500-1000 IOPS
  Low: 1-500 IOPS
  Idle: 0-1 IOPS
Response Time:
  Extremely Slow: 25+ ms
  Very Slow: 10+ ms
  Slow: 5+ ms
  Medium: 2+ ms
  Fast: 0-2ms
Randomness:
  Random: 75-100 Percent Random
  Mixed: 25-75 Percent Random
  Sequential: 0-25 Percent Random
Cache Misses:
  High: 75-100 Percent Misses
  Medium: 25-75 Percent Misses
  Low: 0-25 Percent Misses
IO Size:
  Small: 0-16KB
  Medium: 16-64KB
  Large: 64KB+

## Slide 17: Classification Medium (3) 500+ IOPS
Client | Score | Response Time | Randomness | Cache Misses | IO Size | Front End IOPS | Used (TB)
cdsdbqa | 5 | Medium | N/A | High | Large | 812 | 0.78
sapsb | 4 | Fast | N/A | High | Large | 759 | 5.17
bsmtest | 4 | Fast | N/A | High | Large | 606 | 0.49
Notes: Used Capacity: For Thin Devices, this is the consumed amount of space for each thin devices. For non-thin devices, this is the same as the LUN Capacity and shows the total allocated space.
Front End IOPS:
  High: 1000+ IOPS
  Medium: 500-1000 IOPS
  Low: 1-500 IOPS
  Idle: 0-1 IOPS
Response Time:
  Extremely Slow: 25+ ms
  Very Slow: 10+ ms
  Slow: 5+ ms
  Medium: 2+ ms
  Fast: 0-2ms
Randomness:
  Random: 75-100 Percent Random
  Mixed: 25-75 Percent Random
  Sequential: 0-25 Percent Random
Cache Misses:
  High: 75-100 Percent Misses
  Medium: 25-75 Percent Misses
  Low: 0-25 Percent Misses
IO Size:
  Small: 0-16KB
  Medium: 16-64KB
  Large: 64KB+

## Slide 18: Top Clients by Classification
Chart: Front End IOPS
Chart: Response Time (ms)
Client | # Luns | Used (TB) | Front End IOPS | Response Time (ms) | Cache Hit (%) | Front End MBps | Read % | Avg IO Size (KB)
sjsqlqa10 | 3 | 0.39 | 1,173 | 1 | 0 | 5 | 100 | 8
sjemcrpa01, sjemcrpa02 | 78 | 24.61 | 10,344 | 3 | 0 | 353 | 50 | 71
sapqas01 | 11 | 4.52 | 1,189 | 1 | 0 | 18 | 72 | 51
cdsdbqa | 4 | 0.78 | 812 | 3 | 0 | 29 | 67 | 70
sapsb | 10 | 5.17 | 759 | 0 | 0 | 15 | 89 | 117

## Slide 19: Reduce Your Footprint with Flash
Flash Storage provides the greatest IO density: more IOPS in a small package.
A smaller footprint means reduced power, cooling and floor space requirements.
The consistent performance of flash storage will simplify operational management
Inline deduplication reduces this footprint further, requiring less storage than traditional storage systems without compromising performance.
Drive Type | # Disks | % of IOPS | Raw Capacity (TB) | Raw Capacity (%)
FLASH | 9 | 72 | 2 | 1
SAS | 4 | 4 | 1 | 1
SAS | 45 | 23 | 36 | 22
NL | 48 | 0 | 129 | 77
 | 106 | 100 | 168 | 100

## Slide 20: Analysis

## Slide 21: Front End LUN vs Back End Disk (EFD)
Chart: Front End IOPS
 | 1
Chart: Back End IOPS - EFD Only
 | 1
Chart: Back End IOPS - Disk Only
 | 1
Notes: This is a correlation of FE IOPS, BE EFD IOPS, and BE Disk IOPS. This provides an overview of how the IOPS are spread out across the array.

## Slide 22: IO Size and Read Percent
Chart: Avg IO Size (KB)
Chart: Read %
 | 1
Chart: Front End MBps
 | 1

## Slide 23: IOPS Thresholds
Chart: Front End IOPS
Name | Front End IOPS - avg | Front End IOPS - +1 StdDev | Front End IOPS - 95th | Front End IOPS - max
APM00140712253 | 4,881 | 6,761 | 8,037 | 10,384
Notes: Analyzing and designing for storage workloads requires an understanding of the typical and worst case workloads.
This slide compares three different metrics for estimating workload requirements:
  Front End IOPS - max: Shows the busiest single point in time for all LUN activity.
  Front End IOPS - 95th: The 95th percentile of IOPS. This excludes the top 5% of activity.
  Front End IOPS - +1 Std Deviation: Standard deviation is a statistical concept that measures the variation from an average value.
The Standard Deviation metric is sometimes used by USD and GBS Sizing. Please consult with a USPEED Guru for more information on this metric.

## Slide 24: Back End IOPS by Drive Type
Drive Type | RAID Type | # Disks | Usable (TB) | % of IOPS | Total IOPS - avg | Read IOPS - avg | Write IOPS - avg | Response Time (ms) - avg
FAST Cache |  | 4 |  | 29 | 1,458 | 332 | 1,126 | 0
FLASH 200 | Unknown | 5 | 1 | 43 | 2,213 | 1,442 | 771 | 2
SAS 300 |  | 4 |  | 4 | 223 | 117 | 106 | 2
10K 900 | RAID5,Unknown | 45 | 29 | 23 | 1,183 | 672 | 512 | 11
7K 3000 | Unknown | 48 | 97 | 0 | 16 | 11 | 5 | 16
Back End IOPS are shown here. RAID-5/6 devices will show higher relative values than RAID-1 devices.

## Slide 25: Back End IOPS by Drive Type - Cont'd
Chart: Disk IOPS

## Slide 26: Drive IOPS vs Utilization
Flash drives show the lowest utilization, up to thousands of IOPS. Disk drives will sustain hundreds of IOPS.

## Slide 27: Activity by Client
Chart: Front End IOPS
Chart: Front End MBps
Chart: Response Time (ms)
bsmtest | 1.16 | 0.76 | 1.39 | 2.08 | 1.56 | 1.7 | 1.77
Limited to the Top 8 Clients by Peak IOPS

## Slide 28: Front End IOPS by Host
VBSMBDPRD_Data_RPTGT_4
DW_DATA_RPTGT_7
BSMDBPRD_RP2TGT_0
VBSMDBPRD_Data_RPT
SAPPRD_RPTGT_DA
SAPPRD_RPTGT_LO
INFRADB_RPTGT_2
VBSMBDPRD_Dat
BSMDBPRD_RP2T
RELDBPRD_RPT
DW_DATA_R
DW_DATA_R
DW_DATA_R
VBSMDBPR
CDS_LINU
VBSMD
SAPQA
DW_DA
CDS_LIN
SAPQAS
DW_DA
SAPQA
SAPQ
SAP
VBS
SAP
bsm
DW_
DW_
DW_
CDS
SAP
SAP
SAP
BSM
sjs
VB
CD
SA
BS
SA
SA
SA
VB
SA
BS
SA
V
V
S
bs
VB
SA
IN
SA
vb
VB
re
C
C
cd
IN
R
S
C
S
D
R
IN
R
S
sj
d
c
S
S
I
sjemcrpa01, sjemcrpa02
sapqas01
bsmdbqa01
sjsqlqa10
sapsb
bsmtest
vbsmdbqa
reldbdev
cdsdbqa
armstg01
dwdbqa
Notes:   lun: VBSMBDPRD_Data_RPTGT_4 , iops_avg: 1443.96 , clients: sjemcrpa01, sjemcrpa02
  lun: DW_DATA_RPTGT_7 , iops_avg: 279.92 , clients: sjemcrpa01, sjemcrpa02
  lun: BSMDBPRD_RP2TGT_0 , iops_avg: 277.33 , clients: sjemcrpa01, sjemcrpa02
  lun: VBSMDBPRD_Data_RPTGT_5 , iops_avg: 259.04 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_RPTGT_DATA_7 , iops_avg: 254.86 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_RPTGT_LOG , iops_avg: 227.01 , clients: sjemcrpa01, sjemcrpa02
  lun: INFRADB_RPTGT_2 , iops_avg: 197.05 , clients: sjemcrpa01, sjemcrpa02
  lun: VBSMBDPRD_Data_RPTGT_3 , iops_avg: 164.29 , clients: sjemcrpa01, sjemcrpa02
  lun: BSMDBPRD_RP2TGT_1 , iops_avg: 162.07 , clients: sjemcrpa01, sjemcrpa02
  lun: RELDBPRD_RPTGT_1 , iops_avg: 148.86 , clients: sjemcrpa01, sjemcrpa02
  lun: DW_DATA_RPTGT_5 , iops_avg: 133.15 , clients: sjemcrpa01, sjemcrpa02
  lun: DW_DATA_RPTGT_4 , iops_avg: 104.15 , clients: sjemcrpa01, sjemcrpa02
  lun: DW_DATA_RPTGT_3 , iops_avg: 88.89 , clients: sjemcrpa01, sjemcrpa02
  lun: VBSMDBPRD_Data_RPTGT_1 , iops_avg: 81.53 , clients: sjemcrpa01, sjemcrpa02
  lun: CDS_LINUX_Data_RPTGT_3 , iops_avg: 68.99 , clients: sjemcrpa01, sjemcrpa02
  lun: VBSMDBPRD_Data_RPTGT_6 , iops_avg: 54.33 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPQAS_LINUX_Data_8 , iops_avg: 53.6 , clients: sapqas01
  lun: DW_DATA_RPTGT_1 , iops_avg: 51.64 , clients: sjemcrpa01, sjemcrpa02
  lun: CDS_LINUX_Data_RPTGT_1 , iops_avg: 47.74 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPQAS_LINUX_Data_7 , iops_avg: 46.15 , clients: sapqas01
  lun: DW_DATA_RPTGT_6 , iops_avg: 45.97 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPQAS_LINUX_Data_4 , iops_avg: 39.4 , clients: sapqas01
  lun: SAPQAS_LINUX_Data_3 , iops_avg: 36.58 , clients: sapqas01
  lun: SAPPRD_RPTGT_App , iops_avg: 28.72 , clients: sjemcrpa01, sjemcrpa02
  lun: VBSMBDPRD_Data_RPTGT_2 , iops_avg: 28.31 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_RPTGT_DATA_4 , iops_avg: 28.17 , clients: sjemcrpa01, sjemcrpa02
  lun: bsmdbqa01_lun00 , iops_avg: 26.36 , clients: bsmdbqa01
  lun: DW_DATA_RPTGT_2 , iops_avg: 25.51 , clients: sjemcrpa01, sjemcrpa02
  lun: DW_DATA_JVOL_6 , iops_avg: 21.29 , clients: sjemcrpa01, sjemcrpa02
  lun: DW_DATA_JVOL_5 , iops_avg: 21.25 , clients: sjemcrpa01, sjemcrpa02
  lun: CDS_LINUX_Data_RPTGT_2 , iops_avg: 20.11 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_RPTGT_DATA_5 , iops_avg: 16.3 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPQAS_LINUX_Data_6 , iops_avg: 15.36 , clients: sapqas01
  lun: SAPPRD_RPTGT_DATA_2 , iops_avg: 15.18 , clients: sjemcrpa01, sjemcrpa02
  lun: BSMDBPRD_RP2TGT_2 , iops_avg: 14.6 , clients: sjemcrpa01, sjemcrpa02
  lun: sjsqlqa10-data , iops_avg: 12.77 , clients: sjsqlqa10
  lun: VBSMDBPRD_TGT_JVOL_2 , iops_avg: 12.52 , clients: sjemcrpa01, sjemcrpa02
  lun: CDS_LINUX_Data_RPTGT_4 , iops_avg: 12.37 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_RPTGT_DATA_3 , iops_avg: 12.06 , clients: sjemcrpa01, sjemcrpa02
  lun: BSMDBPRD_2TGT_JVOL_1 , iops_avg: 11.52 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_RPTGT_DATA_6 , iops_avg: 11.38 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPSB-LINUX-App , iops_avg: 10.78 , clients: sapsb
  lun: SAPQAS_LINUX_Data_5 , iops_avg: 10.77 , clients: sapqas01
  lun: VBSMDBPRD_TGT_JVOL_1 , iops_avg: 10.68 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPQAS_LINUX_App , iops_avg: 10.42 , clients: sapqas01
  lun: BSMDBPRD_2TGT_JVOL_2 , iops_avg: 10.33 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_RPTGT_DATA_1 , iops_avg: 10.09 , clients: sjemcrpa01, sjemcrpa02
  lun: VBSMDBPRD_TGT_JVOL_6 , iops_avg: 8.95 , clients: sjemcrpa01, sjemcrpa02
  lun: VBSMDBPRD_TGT_JVOL_5 , iops_avg: 8.9 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_TGT_JVOL_9 , iops_avg: 8.82 , clients: sjemcrpa01, sjemcrpa02
  lun: bsmtest-data_1 , iops_avg: 8.52 , clients: bsmtest
  lun: VBSMDBPRD_TGT_JVOL_3 , iops_avg: 8.44 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPSB-LINUX_Data_8 , iops_avg: 8.16 , clients: sapsb
  lun: INFRADB_TGT_JVOL_1 , iops_avg: 7.41 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPSB-LINUX_Data_6 , iops_avg: 6.94 , clients: sapsb
  lun: vbsmdbqa_data1 , iops_avg: 6.92 , clients: vbsmdbqa
  lun: VBSMDBPRD_TGT_JVOL_9 , iops_avg: 6.6 , clients: sjemcrpa01, sjemcrpa02
  lun: reldbdev-data2 , iops_avg: 6.35 , clients: reldbdev
  lun: CDS_LINUX_TGT_JVOL_2 , iops_avg: 6.3 , clients: sjemcrpa01, sjemcrpa02
  lun: CDS_LINUX_TGT_JVOL_3 , iops_avg: 6.27 , clients: sjemcrpa01, sjemcrpa02
  lun: cdsdbqa_lun4 , iops_avg: 6.24 , clients: cdsdbqa
  lun: INFRADB_TGT_JVOL_2 , iops_avg: 6.08 , clients: sjemcrpa01, sjemcrpa02
  lun: RELDBPRD_TGT_JVOL_2 , iops_avg: 5.78 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_TGT_JVOL_8 , iops_avg: 5.65 , clients: sjemcrpa01, sjemcrpa02
  lun: CDS_LINUX_TGT_JVOL_1 , iops_avg: 5.3 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_RPTGT_DATA_8 , iops_avg: 5.14 , clients: sjemcrpa01, sjemcrpa02
  lun: DW_DATA_JVOL_4 , iops_avg: 5.08 , clients: sjemcrpa01, sjemcrpa02
  lun: RELDBPRD_RPTGT_4 , iops_avg: 4.97 , clients: sjemcrpa01, sjemcrpa02
  lun: INFRADB_RPTGT_1 , iops_avg: 4.87 , clients: sjemcrpa01, sjemcrpa02
  lun: RELDBPRD_TGT_JVOL_1 , iops_avg: 4.66 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_TGT_JVOL_4 , iops_avg: 3.85 , clients: sjemcrpa01, sjemcrpa02
  lun: DW_DATA_JVOL_3 , iops_avg: 3.8 , clients: sjemcrpa01, sjemcrpa02
  lun: sjarmstg01_data1_700gb , iops_avg: 3.7 , clients: armstg01
  lun: dwdbqa_linux_2 , iops_avg: 3.46 , clients: dwdbqa
  lun: cdsdbqa_lun_2 , iops_avg: 3.39 , clients: cdsdbqa
  lun: SAPSB-LINUX_Data_2 , iops_avg: 2.9 , clients: sapsb
  lun: SAPSB-LINUX_Data_7 , iops_avg: 2.79 , clients: sapsb
  lun: RELDBPRD_RPTGT_2 , iops_avg: 2.23 , clients: sjemcrpa01, sjemcrpa02
  lun: INFRADB_RPTGT_3 , iops_avg: 2.17 , clients: sjemcrpa01, sjemcrpa02
  lun: bsmdbqa01_lun01 , iops_avg: 1.96 , clients: bsmdbqa01
  lun: SAPSB-LINUX_Data_4 , iops_avg: 1.95 , clients: sapsb
  lun: SAPSB-LINUX_Data_5 , iops_avg: 1.95 , clients: sapsb
  lun: VBSMDBPRD_TGT_JVOL_4 , iops_avg: 1.89 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_TGT_JVOL_7 , iops_avg: 1.71 , clients: sjemcrpa01, sjemcrpa02
  lun: DW_DATA_JVOL_2 , iops_avg: 1.7 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_TGT_JVOL_1 , iops_avg: 1.7 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_TGT_JVOL_3 , iops_avg: 1.7 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_TGT_JVOL_6 , iops_avg: 1.7 , clients: sjemcrpa01, sjemcrpa02
  lun: DW_DATA_JVOL_1 , iops_avg: 1.69 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_TGT_JVOL_5 , iops_avg: 1.69 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_TGT_JVOL_2 , iops_avg: 1.68 , clients: sjemcrpa01, sjemcrpa02
  lun: UDW_DATA_7 , iops_avg: 1.61 , clients: dwdbqa
  lun: sjarmstg01_data4 , iops_avg: 1.54 , clients: armstg01
  lun: bsmtest-data_2 , iops_avg: 1.38 , clients: bsmtest
  lun: UDW_DATA_4 , iops_avg: 1.3 , clients: dwdbqa
  lun: VBSMDBPRD_TGT_JVOL_8 , iops_avg: 1.06 , clients: sjemcrpa01, sjemcrpa02
  lun: VBSMDBPRD_TGT_JVOL_7 , iops_avg: 1.06 , clients: sjemcrpa01, sjemcrpa02
  lun: cdsdbqa_lun_1 , iops_avg: 0.98 , clients: cdsdbqa
  lun: SAPSB-LINUX_Data_1 , iops_avg: 0.98 , clients: sapsb
  lun: RELDBPRD_RPTGT_3 , iops_avg: 0.98 , clients: sjemcrpa01, sjemcrpa02
  lun: dwdbqa_linux_1 , iops_avg: 0.79 , clients: dwdbqa
  lun: SAPSB-LINUX_Data_3 , iops_avg: 0.63 , clients: sapsb
  lun: sjarmstg01_data3_700gb , iops_avg: 0.61 , clients: armstg01
  lun: dwdbqa_linux4 , iops_avg: 0.45 , clients: dwdbqa
  lun: dwdbqa_linux3 , iops_avg: 0.43 , clients: dwdbqa
  lun: UDW_DATA_6 , iops_avg: 0.39 , clients: dwdbqa
  lun: UDW_DATA_5 , iops_avg: 0.38 , clients: dwdbqa
  lun: sjsqlqa10-backup , iops_avg: 0.24 , clients: sjsqlqa10
  lun: UDW_DATA_3 , iops_avg: 0.2 , clients: dwdbqa
  lun: SAPQAS_LINUX_Archive , iops_avg: 0.15 , clients: sapqas01
  lun: SAPPRD_RPTGT_Ora , iops_avg: 0.09 , clients: sjemcrpa01, sjemcrpa02
  lun: RELDBPRD_RPTGT_5 , iops_avg: 0.08 , clients: sjemcrpa01, sjemcrpa02
  lun: RELDBPRD_TGT_JVOL_3 , iops_avg: 0.07 , clients: sjemcrpa01, sjemcrpa02
  lun: RELDBPRD_TGT_JVOL_4 , iops_avg: 0.07 , clients: sjemcrpa01, sjemcrpa02
  lun: UDW_DATA_1 , iops_avg: 0.02 , clients: dwdbqa
  lun: reldbdev-data1 , iops_avg: 0.02 , clients: reldbdev
  lun: DW_DATA_RPTGT_9 , iops_avg: 0.02 , clients: sjemcrpa01, sjemcrpa02
  lun: DW_DATA_RPTGT_8 , iops_avg: 0.02 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPPRD_RPTGT_DATA_9 , iops_avg: 0.02 , clients: sjemcrpa01, sjemcrpa02
  lun: SAPQAS_LINUX_ORA , iops_avg: 0.01 , clients: sapqas01
  lun: sjarmstg01_data2_700gb , iops_avg: 0 , clients: armstg01
  lun: UDW_DATA_2 , iops_avg: 0 , clients: dwdbqa
  lun: cdsdbqa_lun_3 , iops_avg: 0 , clients: cdsdbqa
  lun: SAPQAS_LINUX_Data_1 , iops_avg: 0 , clients: sapqas01
  lun: SAPQAS_LINUX_Data_2 , iops_avg: 0 , clients: sapqas01
  lun: vbsmdbqa_data2 , iops_avg: 0 , clients: vbsmdbqa
  lun: infradbqas_data_0 , iops_avg: 0 , clients: infradbqas
  lun: infradbqas_data_2 , iops_avg: 0 , clients: infradbqas
  lun: infradbqas_data_1 , iops_avg: 0 , clients: infradbqas
  lun: BSMDBPRD_RPTGT_0 , iops_avg: 0 , clients: bsmdbqa01
  lun: BSMDBPRD_RPTGT_2 , iops_avg: 0 , clients: bsmdbqa01
  lun: BSMDBPRD_RPTGT_1 , iops_avg: 0 , clients: bsmdbqa01
  lun: sjarmstg01_data5 , iops_avg: 0 , clients: armstg01
  lun: bsm-upgradeshare , iops_avg: 0 , clients: bsmdbqa01
  lun: SAPSB-LINUX-ORA , iops_avg: 0 , clients: sapsb
  lun: LUN 400 , iops_avg: 0 , clients: sjemcrpa01, sjemcrpa02
  lun: sjsqlqa10-log , iops_avg: 0 , clients: sjsqlqa10

## Slide 29: Top Clients and LUNs

## Slide 30: Top 15 LUNs by IOPS
LUN | Front End IOPS - max | Front End MBps - max | Avg IO Size (KB) - avg | Response Time (ms) - max | Response Time (ms) - avg | Queue Length - avg - max | Cache Hit (%) - avg | Prefetch Hit (%) - avg | Read % - avg
VBSMBDPRD_Data_RPTGT_4 | 2,990 | 18 | 8 | 4 | 2 | 34 | 0 | 0 | 50
DW_DATA_RPTGT_7 | 2,005 | 3 | 3 | 9 | 2 | 33 | 0 | 0 | 64
DW_DATA_RPTGT_3 | 1,550 | 57 | 54 | 11 | 3 | 34 | 0 | 0 | 64
CDS_LINUX_Data_RPTGT_4 | 1,293 | 75 | 12 | 6 | 0 | 34 | 0 | 0 | 96
DW_DATA_RPTGT_4 | 1,238 | 28 | 36 | 9 | 2 | 35 | 0 | 0 | 67
sjsqlqa10-data | 1,172 | 5 | 6 | 2 | 0 | 1 | 0 | 0 | 8
CDS_LINUX_Data_RPTGT_3 | 1,153 | 22 | 12 | 11 | 2 | 36 | 0 | 0 | 71
CDS_LINUX_Data_RPTGT_1 | 1,048 | 54 | 29 | 20 | 2 | 34 | 0 | 0 | 74
BSMDBPRD_RP2TGT_0 | 1,003 | 6 | 6 | 7 | 2 | 37 | 0 | 0 | 51
DW_DATA_RPTGT_5 | 1,002 | 36 | 44 | 18 | 3 | 34 | 0 | 0 | 64
RELDBPRD_RPTGT_1 | 1,000 | 8 | 13 | 6 | 1 | 36 | 0 | 0 | 70
BSMDBPRD_RP2TGT_1 | 867 | 19 | 32 | 13 | 3 | 35 | 0 | 0 | 51
CDS_LINUX_Data_RPTGT_2 | 799 | 29 | 27 | 39 | 2 | 33 | 0 | 0 | 74
VBSMDBPRD_Data_RPTGT_5 | 614 | 14 | 30 | 6 | 2 | 34 | 0 | 0 | 50
bsmtest-data_1 | 606 | 51 | 14 | 2 | 0 | 1 | 0 | 0 | 4

## Slide 31: Top 15 LUNs by MBPS
LUN | Front End MBps - max | Front End IOPS - max | Avg IO Size (KB) - avg | Response Time (ms) - max | Response Time (ms) - avg | Queue Length - avg - max | Cache Hit (%) - avg | Prefetch Hit (%) - avg | Read % - avg
CDS_LINUX_TGT_JVOL_3 | 101 | 206 | 224 | 33 | 3 | 17 | 0 | 0 | 68
bsmdbqa01_lun00 | 82 | 310 | 133 | 4 | 1 | 19 | 0 | 0 | 33
DW_DATA_JVOL_6 | 77 | 159 | 607 | 14 | 5 | 13 | 0 | 0 | 37
DW_DATA_JVOL_5 | 76 | 158 | 606 | 17 | 5 | 12 | 0 | 0 | 36
CDS_LINUX_Data_RPTGT_4 | 75 | 1,293 | 12 | 6 | 0 | 34 | 0 | 0 | 96
DW_DATA_RPTGT_3 | 57 | 1,550 | 54 | 11 | 3 | 34 | 0 | 0 | 64
CDS_LINUX_Data_RPTGT_1 | 54 | 1,048 | 29 | 20 | 2 | 34 | 0 | 0 | 74
CDS_LINUX_TGT_JVOL_2 | 52 | 118 | 318 | 14 | 2 | 12 | 0 | 0 | 8
CDS_LINUX_TGT_JVOL_1 | 51 | 116 | 257 | 15 | 2 | 13 | 0 | 0 | 10
bsmtest-data_1 | 51 | 606 | 14 | 2 | 0 | 1 | 0 | 0 | 4
VBSMDBPRD_TGT_JVOL_3 | 45 | 96 | 280 | 17 | 3 | 14 | 0 | 0 | 71
bsmtest-data_2 | 44 | 93 | 13 | 5 | 0 | 1 | 0 | 0 | 3
VBSMDBPRD_TGT_JVOL_4 | 37 | 76 | 148 | 16 | 1 | 15 | 0 | 0 | 90
DW_DATA_RPTGT_5 | 36 | 1,002 | 44 | 18 | 3 | 34 | 0 | 0 | 64
CDS_LINUX_Data_RPTGT_2 | 29 | 799 | 27 | 39 | 2 | 33 | 0 | 0 | 74

## Slide 32: Conclusion

## Slide 33: Findings: Good Response Time
Finding
  Peak response time of5.02ms was observed.95% of your IOs were serviced in3.56ms or less.
Impact
  The impact of storage response time varies by application. Imbalanced storage arrays and drive contention can lead to hotspots on specific busy workloads.
Recommendation
  Improving response time begins with ensuring you have a balanced, well-designed infrastructure. Leverage Flash technology to cut response times on the busiest workloads. Replace traditional RAID groups with storage pools.

## Slide 34: Findings: High Skew
Finding
  At a coarse LUN level, your workload ishighly skewed. A large amount of IOs (86%) are going to a small number (15.3285%) of LUNs, with ahighcache hit rate of81.63%.
Impact
  Skewed workloads are a good fit for tiered environments, where "hot" data can be placed on faster storage, and "cold" data can be placed on lower cost storage.
Recommendation
  Tiered storage pools should be employed to promote the busiest workloads to the fastest storage, with the idle workloads on large capacity-oriented drives.

## Slide 35: Findings: High Storage Density
Finding
  We found a storage density of7TB of allocated (LUN) data per shelf, with50TB of LUN data across106drives and7 enclosures.
Impact
  Inefficient, low density environments increase power and cooling costs, as well as leading to more overhead and management.
Recommendation
  Storing more data in a smaller footprint requires more IOPS in the same footprint. To achieve this, leverage dense drive enclosures for your performance-oriented workloads, and large-capacity NL-SAS drives for your capacity-oriented workloads.

## Slide 36: Findings: Low CPU Utilization
Finding
  CPU Utilization peaked at14.48%.
Impact
  Overloaded or imbalanced CPUs will adversely affect all storage operations, including IO response time and background activities.
Recommendation
  CPU utilization is not a major concern at this time.

## Slide 37: Appendix

## Slide 38: Input Files
Filename | Start Date | End Date
APM00140712253_SPA_2015-02-01_02-57-28-GMT_M08-00.nar | 2015-01-31 14:04 | 2015-02-01 02:54

## Slide 39: Pools and LUNs
Type | Capacity (TB) | # Luns | Average IOPS
Thick | 30 | 80 | 4,018
Thin | 20 | 57 | 863
 | 50 | 137 | 4,881
Parent | # Luns | LUNs (TB) | Used Capacity (TB) | % IOPS
Pool 0 - Recoverpoint JVol | 21 | 3 | 3 | 2
Pool 1 | 116 | 47 | 47 | 98
 |  | 50 | 50 | 100
Notes: LUN Capacities for "thin" luns is the consumed size of the LUN.

## Slide 40: Cache Hit %
Chart: Cache Hit (%)
 | 1

## Slide 41: Queue Length Average
Chart: Queue Length - avg
 | 1

## Slide 42: Thank You